Object-oriented modelling
of multi-rotor vehicle dynamics
Metodologie ICT per i Sistemi di Controllo – A.A. 2013/2014
March 26th, 2014
Marcello Pogliani – Davide Tateo
[Speaker Notes: Good morning, my name is Marco Bergamasco and today I’ll show you the work that I’ve done with Prof. Marco Lovera and Fabio Beltramini about the “Experiment Design for MIMO Model Identification with Application to Rotorcraft Dynamics”]

---
Objectives
This project
1. Design and implementation of basic components
   for the particular case of fixed pitch (variable rpm) quadrotor
3. Tool: OpenModelica [1]
5. In particular:
- Modelica Multibody library (basic rigid body dynamics, gears, etc)
- Modelica Electrical library for motors
- Simple models for rotor force/torque generation mechanisms [2]
- Existing implementations for control algorithms (PI control)

---
Approach
1. Familiarisation with the system
2. Hierarchical breakdown into subsystems and definition of interfaces
3. Development of models for individual components
4. Development and testing of simulator

---
Familiarisation with the system
Main components
Structure (metallic tubes)
Power system (battery, power
electronics)
On-board computer (including
sensors)
Motor drivers
Motors
Propellers

---
Hierarchical breakdown into subsystems and definition of interfaces
Frame interface
+ signal bus
PI controller set point
(target ω for each arm)
Rotor
Chassis
& controller
Flange + frame
Arm
Quadrotor (variant for n-rotor)

---
The Multirotor package

---
Models for individual components
Rotor
1. Leverages a simple model from [2] to compute lift and drag
7. Incorporates the model of an inertia (from the Modelica standard library)
9. Interfaces:
- Frame to the rigid body of the arm
  (transmit the lift)
- Flange to the motor
  (transmit the torque)
L = %alpha cdot bl cdot %omega^2 newline newline Tl = sign( %omega ) cdot left ( bd_1 %omega^2 + bd_2 %omega^2 %alpha^2 + bd_3 cdot abs %omega cdot %alpha right )
Parameters:
α = 10°
bd[] = {9.96e-09,2.46e-10,4.33e-07}
bl = 3.88e-07
Jr = 3.5e-05 kg · m2 (rotor inertia)

---
Models for individual components
PartialArm
- Rigid body (from the Multibody library)
- Gear (ideal)
- Bus connection: speed sensor signal [rad/s] + control signal [V]
- Signal-controlled voltage generator
Arm extends PartialArm with:
- Connection to a DC_PermanentMagnet motor
- Connection to a Rotor model (see previous slide)
Motor:
motorVoltage = 12 V
motorResistance = 0.3 ohm
motorInductance = 0.0015 H
motorVelocity = 1100 rad/s
motorInertia = 3.5e-05 kg · m2
rotorInertia = 3.5e-05 kg · m2
Arm (rigid body):
length = 0.2 m
diameter = 0.01 m
mass = 0.18 kg
Gear:
gearRatio = 1

---
Models for individual components
Chassis / ChassisNRotor
- Rigid body to model the weight of the central support + microcontroller + …
- Connect all the arms through Frames, taking into account the correct orientation (using a FixedRotation component)
Controller
- A set of PI controllers, one per arm
- Directly connected to the arms through Bus connections
- Set point: the desired angular speed

---
Development and testing of the simulator
Developed simulations (package Examples):
10. Notice: the set point is the angular velocity of each arm; it is easy to attach a more complex control system to the simulator in order to provide a more significant input (set point) in terms of roll\pitch\yaw
TestYaw
TestRollPitch
TestQuadrotor
[Speaker Notes: It has four independent rotors and you can see how it is possible to combine the rotors to obtain collective, pitch, roll and yaw motions]

---
References
1. [1] OpenModelica, https://www.openmodelica.org/
2. [2] M. J. Cutler, Design and Control of an Autonomous Variable-Pitch Quadrotor Helicopter, Master's Thesis, Massachusets Institute of Technology, September 2012
3. [3] P. Fritzson et al., OpenModelica Users Guide, March 2014
4. [4] P. Fritzson and O. Rogovchenko, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial at MODPROD, February 2012
5. [5] Modelica® - A Unified Object-Oriented Language for Physical Systems Modeling, Language Specification, Version 3.2, March 2010